## Slide 1
HD-SDI IR BULLET CAMERA
USER’S MANUAL
• 1/3” Sony CMOS (IMX138)
• Digital : 1280x720p(720p/60fps)
• Min. Illumination of 0.001Lux(Sense-up x32)
• True Day & Night
• NTSC/PAL selectable
• Defog(Visibility enhancement on the low contrast scene)
• High resolution digital zoom (x8)
• 2D & 3D Digital Noise Reduction
• Flicker Suppression
• Motion Detection, Privacy Masking (16 Zone)
• 30pcs IR LED
• 2.8~12.0mm Megapixel ICR V/F Lens
• IP66 Weatherproof
• Option : RS-485 / OSD Controller
FEATURES
SDI-UL221IRV
MEMO
SPECIFICATIONS
* In accordance with customers’ request and OSD controller’s option, the specifications can be fixed or changed without notice.
Off / Low / Middle / High
DNR
BRIGHTNESS
0 ~ 20 steps
Min. illumination
Color : 1.0 lux , BW : 0.5lux, Color DSS : 0.002 lux , BW DSS : 0.001 lux
Active pixels
1305(H) x1049(V) = 1.37M (pixel)
Scanning system
Progressive Scan
1/3” Sony CMOS(IMX138)
Image Sensor
-10°C ~ +50°C
Operating Temperature
0% ~ 90%
Operating Humidity
79.2(W) x 74.7(H) x 146.3(D)mm
Dimension
30 pcs
IR LED
DC 12V (±10%)
Power Supply
LED Off : Max. 150mA / LED On : Max. 400mA
Power Consumption
2.8~12.0mm Megapixel ICR V/F Lens
Lens
Digital ; 1280x720p(720p/60fps)
Resolution
On / Off
MIRROR
SDI-UL221IRV
S/N Ratio
HD-SDI, Analog : NTSC, PAL(without WDR)
Video Output
SENS-UP
0~20 steps
AGC
On / Off
DEFOG
Off / HLC / BLC / WDR
BACKLIGHT
Approx. 888g (W/ Sunshield & Bracket)
Weight
1312(H) x 1069(V) = 1.4M (pixel)
Total Pixels
On / Off
D-WDR
On / Off
SHADING
On(16 Points) / Off
PRIVACY
On / Off
MOTION
50FPS / 60FPS
FRAME RATE
NTSC/PAL
CVBS
ENG/CHN/JPN (Multi Language)
Language
Auto / Autoext / Preset / Manual
WHITE BALANCE
0 ~ 10 steps
SHARPNESS
more than 50dB (AGC off)
Off / x2 / x3 / x4 / x5 / x6 / x7 / x8 ~ x32
On / Off
FLIP
Auto / Color / B&W / Ext
DAY&NIGHT
SHUTTER SPEED
Auto / Flicker / Manual (1/60(50)~1/6000)

## Slide 2
PRECAUTIONS
• Do not install the camera in extreme temperature conditions. - Only use the camera under conditions where temperatures are between -10°Cand +50°C. Be especially careful to provide ventilation when operating under high temperatures.
• Do not install or use the camera in an environment where the humidity is high. - It can cause the image quality to be poor.
• Do not install the camera under unstable lighting conditions. - Severe lighting change or flicker can cause the camera to work improperly.
• Never use the camera close to a gas or oil leak. - It can cause malfunctions to occur.
• Do not disassemble the camera. - There are no user-serviceable parts inside it.
• Do not touch the front lens of the camera. - It is one of the most important parts of the camera. Be careful not to be stained by fingerprint.
• Never keep the camera face to strong light directly. - It can damage the image sensor.
• Do not drop the camera or subject them to physical shocks. - It can cause malfunctions to occur.
• Do not expose the camera to rain or spill beverage on it. - If it gets wet, wipe it dry immediately. Liquids can contain minerals that corrode the electronic components.
• Do not expose the camera to radioactivity. - If exposed to radioactivity the image sensor will fail.
* NOTE *
• If the camera is exposed to spotlight or object reflecting strong light, smear or blooming may occur.
• Please check that the power satisfies the normal specification before connecting the camera.
COMPOSITION
NAME OF EACH PART
Lens
Bracket
Camera
Video cable
Power cable
Screw
Manual
L- Wrench
Sunshield
IR LED
Sensor
CABLE CONNECTION
DIMENSION
a. SET : Displays the menu on the screen. Press this switch to confirm status or after changing a selected item.
b. UP / DOWN : Used to move the cursor up or down in the menu screen to select a desired menu item.
c. LEFT / RIGHT : Used to move the cursor left or right in the menu screen or to change the value of the selected item.
OSD CONTROL (Option- BOARD / CABLE)
Video loop-out
OSD Controller
UP
DOWN
R
L
a
HD-SDI output
Power input (DC 12V)
Video cable (Option)
Red : RS-485+ / Yellow : RS-485- White : Motion output / Black : GND (Option)