## Slide 1
HD-SDI COLOR IR LED CAMERA
USER’S MANUAL
• 1/3” Panasonic 2.1M Pixel Progressive Scan Color CMOS Sensor
• 1944x1092@30fps
• Video Out (BNC) with NTSC/PAL Selectable
• Dual Output – Megapixel HD CCTV (BNC) and SD CCTV (BNC) out
• Defog (Visibility Enhancement on the Low Contrast Scene)
• Digital Zoom (x8)
• Sens-up (x8)
• Flicker Suppression
• DNR (2D & 3D Noise Reduction)
• DPC (Dead Pixel Compensation)
• 2 Auto (AE/AWB) Control
• HLC/BLC Support (High Light / Back Light Compensation)
• 54pcs IR LED
• 6.0mm Megapixel Fixed Lens
• IP66 Weatherproof
• Option : RS-485 / OSD Controller
FEATURES
SDI-UL252IR
MEMO
SPECIFICATIONS
* In accordance with customers’ request and OSD controller’s option, the specifications can be fixed or changed without notice.
6.0mm Megapixel Fixed Lens / Built-In TDN
Lens
Sens-up
ON / OFF (~ x8)
Electronic Shutter Speed
AUTO / FLK NTSC : 1/30~1/60,000sec PAL : 1/25~1/50,000sec
Video Output Mode
1080P (1920x1080) 25P/30P
Total Pixels
2010(H) x 1108(V)
Effective Pixels
1944(H) x 1092(V)
Image Sensor
1/3” 2.1Megapixel CMOS
-10°C ~ +50°C
Operating Temperature
Less than 90%
Operating Humidity
79.7(W) x 79.3(H) x 117.1(D)mm
Dimension
54 pcs
IR LED
DC 12V (±10%)
Power Supply
LED Off : Max. 2.3W / LED On : Max. 7.5W
Power Consumption
More than 50dB
S/N Ratio
ON / OFF (16 Zone Selectable)
Privacy Masking
SDI-UL252IR
Video Output Level
Color : 0.5Lux (B/W : 0.1Lux / Sens-up x8 : 0.02Lux)
Min. Illumination
White Balance
BLC / HLC / WDR / OFF
Backlight Compensation
ON / OFF
D-WDR
0 ~ 20
AGC
Approx. 794g (W/ Sunshield & Bracket)
Weight
Progressive Scan
Scanning System
MIRROR / D-ZOOM / FLIP
D-Effect
720P / 720P CROP / 1080P
Output Mode
1080P-25FPS / 30FPS , 720P CROP-50FPS / 60FPS
Frame Rate
English (Selectable)
Language
Built-in
OSD
OFF / LOW / MIDDLE / HIGH
DNR
ON / OFF
Motion Detection
HD-SDI / 1.0Vp-p (75Ω, Composite) NTSC/PAL (W/O WDR)
AUTO / AUTOEXT / PRESET / MANUAL
ON / OFF
Defog
AUTO / BW / COLOR / EXT (Selectable)
Day & Night

## Slide 2
PRECAUTIONS
• Do not install the camera in extreme temperature conditions. - Only use the camera under conditions where temperatures are between -10°Cand +50°C. Be especially careful to provide ventilation when operating under high temperatures.
• Do not install or use the camera in an environment where the humidity is high. - It can cause the image quality to be poor.
• Do not install the camera under unstable lighting conditions. - Severe lighting change or flicker can cause the camera to work improperly.
• Never use the camera close to a gas or oil leak. - It can cause malfunctions to occur.
• Do not disassemble the camera. - There are no user-serviceable parts inside it.
• Do not touch the front lens of the camera. - It is one of the most important parts of the camera. Be careful not to be stained by fingerprint.
• Never keep the camera face to strong light directly. - It can damage the image sensor.
• Do not drop the camera or subject them to physical shocks. - It can cause malfunctions to occur.
• Do not expose the camera to rain or spill beverage on it. - If it gets wet, wipe it dry immediately. Liquids can contain minerals that corrode the electronic components.
• Do not expose the camera to radioactivity. - If exposed to radioactivity the image sensor will fail.
* NOTE *
• If the camera is exposed to spotlight or object reflecting strong light, smear or blooming may occur.
• Please check that the power satisfies the normal specification before connecting the camera.
NAME OF EACH PART
Lens
Bracket
Sunshield
IR LED
Sensor
DIMENSION
COMPOSITION
Camera
HD-SDI cable
Power cable
Screw
Manual
RS-485 cable (Option)
a. SET : Displays the menu on the screen. Press this switch to confirm status or after changing a selected item.
b. UP / DOWN : Used to move the cursor up or down in the menu screen to select a desired menu item.
c. LEFT / RIGHT : Used to move the cursor left or right in the menu screen or to change the value of the selected item.
CABLE CONNECTION
HD-SDI output
Power input (DC 12V)
Red : RS-485+ / Yellow : RS-485- White : Motion output / Black : GND (Option)
OSD CONTROL (Option- BOARD / CABLE)
Video loop-out
OSD Controller
UP
DOWN
R
L
a